Danny Barnes
ECE 375 / R 10am-12pm
February 9th, 2017

Lab 5 Prelab

1. Add, subtract, and multiply operations:
  1. ADC – adds two 8-bit registers and adds the carry bit
  2. ADD – adds two 8-bit registers without considering carry bit
  3. ADIW – adds a 6-bit constant to a 16-bit register pair
  4. DEC – decreases an 8-bit register by 1
  5. FMUL – multiplies two 8-bit registers as unsigned fractional numbers
  6. FMULS – multiplies two 8-bit registers as signed fractional numbers
  7. FMULSU – multiplies two 8-bit registers with one as a signed fractional number and the other as an unsigned fractional number
  8. INC – increases an 8-bit register by 1
  9. MUL – multiplies two 8-bit registers as unsigned numbers
  10. MULS – multiplies two 8-bit registers as signed numbers
  11. MULSU – multiplies two 8-bit registers with one as a signed number and the other as an unsigned number
  12. SBC – subtracts two 8-bit registers and subtracts the carry bit
  13. SBCI – subtracts an 8-bit constant from an 8-bit register and subtracts the carry bit
  14. SBIW – subtracts a 6-bit constant from a 16-bit register pair
  15. SUB – subtracts two 8-bit registers without the carry bit
  16. SUBI – subtracts an 8-bit constant from an 8-bit register without the carry bit
2. Pseudocode for 16-bit add from data memory:
Load to registers from $0111, $0110, $0121, $0120
Add registers with data from $0110, $0120
Add with carry registers with data from $0111, $0121
Store first result in $0100
Store second result in $0101
Pseudocode for 16-bit subtract from data memory:
Load to registers from $0111, $0110, $0121, $0120
Subtract the $0110 data register from the $0120 data register
Subtract with carry the $0111 data register from the $0121 data register
Store first result in $0100
Store second result in $0101